## Slide 1
Early DR (grades 1–2) on DDR, EyePACS and APTOS fundus images
Advisor: Navid Amini, PhD
Department of Computer Science
Early Detection of Diabetic Retinopathy
1

## Slide 2: About Diabetic Retinopathy
The clinical burden is growing
Diabetes has expanded rapidly worldwide, increasing the number of people who need retinal screening for diabetic retinopathy.
151M
adults living with diabetes in 2000
589M
adults living with diabetes in 2024
+290%
observed increase in screening population
Observed growth over time
More patients means more fundus images to grade - and more pressure for fast triage.
2

## Slide 3: Research Aim
Catch early DR (grades 1–2)
Many studies target referable DR (moderate or worse). This thesis targets the earliest grades.
Fundus photo
Deep learning
Early-DR flag (1–2)
Referral / review
Primary Sensitivity for grades 1–2 vs No DR at a fixed specificity.
Secondary Separate early (1–2) from late (3–4) DR for triage.
Robustness Held-out EyePACS patients, then APTOS, never used in training.
Goal: high sensitivity at fixed specificity, with calibrated probabilities.
3

## Slide 4
PROGRESS · MEASURED ON THE REAL DDR + EYEPACS LABELS
The EyePACS merge has a measurable cost
Topping up only the short grades links “which dataset” to “how severe”. Measured from the label files alone — no images, no GPU, no training.
SHARE OF EACH GRADE TAKEN FROM EYEPACS
Grade 0
0.0%
Grade 1
79.0%
Grade 2
0.0%
Grade 3
78.7%
Grade 4
43.7%
0.512 bits
of the severity label is recoverable from the dataset name alone — 24.6% of its information
100%
of merged EyePACS images carry disease, so 38.7% of all disease cases are identifiable purely by recognising the camera
0.167 → 0.000
score of a dataset-name-only predictor: under a random split, versus in a single-clinic test
The shortcut is specific to the earliest decision — any disease versus none (AUC 0.694), and useless for referable disease (0.482).
That is exactly the decision this thesis targets, so the merge must be audited rather than assumed safe.
Design consequence: three arms — A (DDR only), B (source-balanced) and C (this merge, kept as a negative control) — with every result reported per source.
4
Notes: This is what I have measured so far, and it changed the design of the project. Because the top-up is applied only to the short grades, grades 0 and 2 contain no EyePACS images while grades 1 and 3 are nearly 80 percent EyePACS. A quarter of the severity label is recoverable from the dataset name alone. Every merged EyePACS image carries disease, so a model that learns only to recognise the camera gets 38.7 percent of disease cases right with no false alarms — and only for the earliest decision, which is the one I am targeting. So the merge is not just an imbalance fix; it has a cost, and the thesis now measures it.

## Slide 5: Proposed Methods
Three data arms, one change at a time
Same model, image size and epochs; frozen patient-level splits; test sets opened once.
Data DDR, EyePACS, APTOS
Prepare Crop, pad, 512 px
Merge arms A, B, C
Model EfficientNet-B0
Output Calibrated, 95% CI
Imbalance methods tested
Weighted sampler
Class-balanced loss
Focal loss
Strong augmentation
Augmentation control
The three arms
• A: DDR only (clean baseline)
• B: DDR + EyePACS, source-balanced
• C: version 1 merge (negative control)
• C wins on its own test but not on APTOS = it learned the source
Not a new network: the value is the design, the controls and the evidence.
5

## Slide 6: Complete Model Architecture
From fundus image to a calibrated early-DR flag
6
TRAIN: one model per arm, task and seed
Fundus image
DDR, EyePACS, APTOS; frozen patient-level splits
Preprocess
Crop border, pad to square, resize to 512 px (colour norm optional)
Sampler + augment
Arm B: source-balanced. Weighted, class-aware or repeat-factor. Mild or strong
Backbone
EfficientNet-B0, ImageNet weights (ViT + RETFound as extension)
Head (1 per run)
0 vs 1-4, early vs late, 3-class or 5-grade
Loss
Cross-entropy, class-balanced CE, or focal (gamma 1-3)
VALIDATE AND FREEZE, THEN TEST
Best epoch
Chosen on validation score only
Temperature scaling
One number T, fitted on validation
Prior-shift correction
Training class mix back to natural prevalence
Frozen threshold
Set at the declared specificity (0.90) on validation
Outputs
Calibrated probability, early-DR flag, per-source metrics with 95% CI
Test sets opened once: DDR + held-out EyePACS, then APTOS last. Grad-CAM with a randomised-weights check.

## Slide 7
Expected contribution & impact
No accuracy gain is promised in advance: the value is in the design and the evidence.
Early-first
evidence
A tested
merge
Controlled
comparison
Calibrated
outputs
What I will show
• Early-DR sensitivity at fixed specificity, with CIs
• Does EyePACS help, or only teach the source?
• Sampler, loss, augmentation: one change at a time
• Calibrated probabilities on unseen sources
How it will be measured
Sensitivity at 90% specificity
PR-AUC and AUROC
ECE and Brier score
Held-out EyePACS patients
APTOS (external, last)
Grad-CAM sanity check
Takeaway: a controlled, calibrated test of early-DR screening across datasets.
7

## Slide 8: Next Steps
Pipeline built and tested on synthetic data; real-data runs are next
1
Train
Arms A, B and C on DDR and EyePACS, 3 seeds
2
Compare
Imbalance ablations, chosen on validation only
3
Test
Held-out EyePACS patients, then APTOS (last)
4
Write
Grad-CAM check, thesis chapters
Goal: evidence that early-DR screening holds across datasets, with probabilities that can be trusted.
8

## Slide 9: References
• International Diabetes Federation. IDF Diabetes Atlas, 11th ed., 2025.
• Ting, D. S. W., et al. 'Artificial intelligence-assisted diabetic retinopathy screening.' Ophthalmology, 2021.
• Shah, P., et al. 'Progression of DR and screening demand.' JAMA Ophthalmology, 2024.
• WHO. Guidelines on diabetic retinopathy screening, 2023.
• CDC. Eye-health guidance for people with diabetes, 2024.
• Li, T., et al. Diagnostic assessment of deep learning algorithms for DR screening (DDR). Information Sciences, 2019.
• Kaggle. Diabetic Retinopathy Detection (EyePACS), 2015; APTOS 2019 Blindness Detection.
• Guo, C., et al. On calibration of modern neural networks. ICML, 2017.
• Sipka, T., et al. The hitchhiker’s guide to prior-shift adaptation. WACV, 2022.
9

## Slide 10: THANK YOU
Questions? We’d love to discuss!